## Slide 1: MICROSPHERE
Microsphere is a bluetooth synth controller, designed to familiarize with diatonic harmony.

## Slide 2: INDEX
Concept
How does it work:
- BLE connection
- Algorithms
- Synthetiser
3. Interface

## Slide 3: CONCEPT

## Slide 4: INTRODUCTION
The foundamental need for a musician is to learn how to express himself, how to transmit to an audience what he’s feeling. There are several key skills to achieve, MicroSphere works on one of them: get used to how notes (and scales) sound on different chords.

## Slide 5: BASED ON SCALE BRIGHTNESS…
Literature tells that in major harmony a quality for perceived mood of scales can be defined: brightness. Scales can be ordered, from darkest to brightest as: locrian, phryigian, aeolian, dorian, mixolydian, ionian, lydian. (Order is based on lowering intervals too.) Due to Micro:bit’s limitations(*) returned scales can be 2.
The algorithm gives the user the two darkest modes matching the seventh chord that is being played. The idea is to facilitate exploration of the more unused scales of major harmony.

## Slide 6: …AND ON SEVENTH CHORDS SPECIES
Major third, perfect fifth, minor seventh: it calls for a mixolydian scale built on first grade. Locrian on 3° grade and Phrygian on the 6° are preferred;
Minor third, perfect fifth, minor seventh: min7th chord have lots of compatible scales, so that, phrygian and aeolian built on the first grade are returned;
Minor third, diminished fifth, minor seventh: locrian scale is the characteristic one of this chord, phrygian on the 4° grade is the other one chosen;
Major third, perfect fifth, major seventh: lydian and ionian scales are typical, following the principle of the application, 3° grade phrygian and 7° locrian are returned.

## Slide 7
GRADE CHORD | First Sharpened | Second Sharpened | Third Sharpened | Fourth Sharpened | Fifth Sharpened | Sixth Sharpened | Seventh Sharpened
X7 | Mixolydian | Aeolian | Locrian | Ionian | Dorian | Phrygian Lydian | 
Xmin7 | Dor, Phr, Aeol Lydian | Locr, Phry Ionian, Lydian |  | Mix, Dor, Aeol | Locr, Phr, Aeol Ionian, Lydian | Locrian Ion, Dor, Mix | 
Xmin7/b5 | Locrian Ionian | -- Dorian |  | Phrygian Lydian | -- Mixolydian | -- Aeolian | 
Xmaj7 | Ionian, Lydian | Mix, Dor | Phry, Aeol | Lydian Locrian | Mixolydian | Dor, Aeol | Locrian
TABLE OF CHORDS AND MATCHING SCALES

## Slide 8: HOW DOES IT WORK

## Slide 9: CODE DIVISION
BLE connection routine;
PROCEDURE II: chord acquirement and elaboration;
Returned scales are associated to Micro:bit’s accelerometer values;
Accelerometer values that are mapped on 3 axis: z>0 is necessary for the synth to be triggered, tilting is associated to notes, pitching is associated to scale changes;
Mapped accelerometer values trigger WAPI synthetiser;
Interface reacts on synth and scales behaviour.

## Slide 10: BLE CONNECTION ROUTINE
Based on client(MB)/server(PC) model, where the PC asks for Micro:bit data;
Bluetooth Low Energy antenna is implemented in Micro:bit;
The firmware activates the needed antenna services on start of the microprocessor;
The code generates a window to trigger the search for available BLE devices;
No pairing is required by firmware, connection is established;

## Slide 11: PROCEDURE II
A seventh chord is played on the MIDI keyboard;
MIDI notes are scanned;
The lowest is supposed as root;
The seven modes are generated starting from the root note;
Matches between the scales and the chord notes are found;
Two darkest scales from 2nd octave to 4th octave are returned.

## Slide 12: ENVIRONMENT
MicroSphere is a web application;
Languages used for coding are: javascript, css and html;
Google Chrome is needed to launch the program. Google’s browser is the only one supporting experimental browser features, needed for BLE connection;
Firmware in Microbit is the Lancaster University one, developers of the microprocessor.

## Slide 13: WAPI SYNTHETISER
BLOCK DIAGRAM

## Slide 14
Gain Modulator
Oscillator
Oscillator Gain
Filter
Envelope
(Gain)
Mod. Filter Gain
Effect Chain??
Distortion
Delay
Effect Chain
Modulator
Oscillator
Gain Delay
Convolver
Rev. Dry Gain
Rev. Wet Gain
Master Gain
Compressor
Analyzer
Context Destination
- Current Env. Decay
- Current Env. Sustain
- Current Env.
- Env
- Type
- Oscillator value
- Frequency
- Detune
- Freq.
- Type
Connect (Osc. Freq)
Gain = FilerGain * 24
Connect (Filter Detune)
- Freq.
- Type

## Slide 15: INTERFACE
Wide screen: where melodic contour is visualized. Head of trace dimension varies on wrist postion, associated with scale brightness. Head of trace position depends on note’s keyboard position. Trace depends on selected scale.
«MIDI» led: on if MIDI notes are received from keyboard;
«Search device» button: BLE connection routine begins;
«Fullscreen» button: visualization page goes full screen;
«Start» button: melodic contour visualization begins;
«Reset» button: melodic contour visualization resets;

## Slide 16: INTERFACE
A keyboard displays which of the piano notes between 2nd and 4th scale are played.

## Slide 17: INTERFACE: CONTROL PANEL
«Osc. Waveform» slider
«Mod waveform» slider
«Master» fader
«Distortion» controls: drove, dist curve, q factor, oversample…. Space: delay time, delay gain, reverb